## Slide 1: Secure Modem
Hardware Design – Vocoder Communication Interface

## Slide 2: Contents
Vocoder Block Diagram
Communication Interface
Interface Selection
Summary
Discussion

## Slide 3: Vocoder Block Diagram

## Slide 4: Vocoder Block Diagram
Basic communication to/from vocoder:
  Input digitized speech data samples
  Input compressed speech data
  Output digitized speech data samples
  Output compressed speech data

## Slide 5: Communication Interface
Vocoder Operation Modes
Vocoder Interface

## Slide 6: Vocoder Operation Modes
Codec Mode
  Transmit and receive digitized voice to and from audio codecs, use either SPI or McBSP interface
  Compressed channel uses one of the remaining interfaces
  Packets containing channel data are sent and received every 20 ms
Packet Mode
  Both digitized voice and compressed channel are on the same interface
  Vocoder sends a packet in response to every packet received
Notes: Notes:
Packet mode
  Control packet received will be responded with control response packet
  Speech packet received will be responded with channel packet
  Channel packet received will be responded with speech packet
Source:
http://www.dvsinc.com/products/a3000.htm
AMBE-3000F_manual.pdf

## Slide 7: Vocoder Interface
Four physical interfaces:
  SPI
  McBSP
  UART
  Parallel
Interface Configurations |  | 
Mode | Codec Interface | Packet Interface
Codec | SPI | UART
Codec | SPI | PPT
Codec | SPI | McBSP*
Codec | McBSP* | UART
Codec | McBSP* | PPT
Packet | - | UART
Packet | - | PPT
Packet | - | McBSP*
Notes: Notes:
McBSP interface may be used for codec interface or the packet interface but not both

## Slide 8: Vocoder Interface 1
SPI
  A high-speed, synchronous serial I/O port that can be used as the speech interface to the audio codec
  It is designed for speech data only and may be used only in codec mode
  SPI pinout
Pin Name | Direction | Description
SPI_CLK | Input | A/D serial clock
SPI_STE | Input | Framing signal generated from pin SPI_GENSTE
SPI_RX_DATA | Input | PCM data from audio codec to vocoder
SPI_TX_DATA | Output | PCM data from vocoder to audio codec
Notes: Notes:
SPI (Serial Peripheral Interface)
Source:
AMBE-3000F_manual.pdf

## Slide 9: Vocoder Interface 2
UART
  A serial interface that supports asynchronous communication of real-time compressed voice data to other asynchronous peripherals
  It is designed for packet data only
  If used on codec mode, the interface provides only channel data. If used on packet mode, the interface provides both speech and channel data
  UART pinout
Pin Name | Direction | Description
UART_TX | Output | UART transmit data
UART_RX | Input | UART receive data
Notes: Source:
AMBE-3000F_manual.pdf

## Slide 10: Vocoder Interface 3
McBSP (Multichannel Buffered Serial Port)
  A synchronous serial communication port
  It can be used as either the codec interface or the packet interface, but not both
Pin Name | Direction | Description
McBSP_RxD | Input | Serial receive data
McBSP_TxD | Output | Serial transmit data
McBSP_CLKR | Input | Serial receive clock
McBSP_FSX | I/O | Serial transmit frame
McBSP_CLKX | I/O | Serial transmit clock
McBSP_FSR | Input | Serial receive frame

## Slide 11: Vocoder Interface 4
Parallel
  The interface runs asynchronously and allows all packet data transfers to be performed on an 8-bit wide bus.
  It is designed for packet data only
  If used on codec mode, the interface provides only channel data. If used on packet mode, the interface provides both speech and channel data
Pin Name | Direction | Description
PPT_DATA[0:7] | I/O | Parallel data port
PPT_READ | Input | PPT read request
PPT_WRITE | Input | PPT write request
PPT_ACK | Output | PPT transfer ack

## Slide 12: Interface Selection

## Slide 13: Secure Modem Requirement
Able to record and play audio (thus need audio codec)
Easily connected to controller/minicomputer (has USB interface)

## Slide 14: Interface Selection
Interface Configurations |  |  | 
Mode | Codec Interface | Packet Interface | Reasoning
Codec | SPI | UART | SELECTED
Codec | SPI | PPT | Require many pinout
Codec | SPI | McBSP* | Non std interface
Codec | McBSP* | UART | Non std interface
Codec | McBSP* | PPT | Non std interface
Packet | - | UART | No codec
Packet | - | PPT | No codec
Packet | - | McBSP* | No codec
SELECTED because UART interface can be converted easily to USB interface

## Slide 15: Secure Modem Interface Design
Secure Modem:
  Codec interface: SPI
  Packet interface: UART
  Controller interface: USB

## Slide 16: Summary

## Slide 17: Communication Interface
Vocoder communicates with audio codec (codec interface) and controller (packet interface)
Operation modes of AMBE vocoder: codec mode and packet mode
Codec mode: select two physical interfaces (one for codec data and packet data)
Packet mode: select one physical interface to receive and transmit packet data

## Slide 18: Communication Interface 1
Interface configurations
Secure modem interface design
Interface Configurations |  | 
Mode | Codec Interface | Packet Interface
Codec | SPI | UART
Codec | SPI | PPT
Codec | SPI | McBSP*
Codec | McBSP* | UART
Interface Configurations |  | 
Mode | Codec Interface | Packet Interface
Codec | McBSP* | PPT
Packet | - | UART
Packet | - | PPT
Packet | - | McBSP*

## Slide 19: Discussion