## Slide 1: Secure Modem
Hardware Design – Vocoder Special Function

## Slide 2: Contents
VAD and CNI
Echo Canceller
DTMF Detection and Generation
Soft Decision Error Correction
Noise Suppressor
Companding Using A-Law and U-Law
Summary
Discussion
Notes: Notes:
Voice Activity Detection and Comfort Noise Insertion
DTMF (Dual Tone Multiple Frequency)

## Slide 3: VAD and CNI

## Slide 4: Block Diagram
Period of silence detected on speaker side
VAD enabled vocoder generates silent frame
The silent frame detected by CNI enabled vocoder
The vocoder generate comfort noise on listener side

## Slide 5: Description
The VAD and CNI are useful functions that trying to convert periods of silence, that exist in normal conversation, to saving in system bandwidth
When enabled, VAD detects periods of silence and will output a silence frame
The silence frame contains info regarding the level of background noise, which allows the corresponding decoder to synthesize a comfort noise signal at listener side

## Slide 6: Description 1
The comfort noise is intended to give listener a feeling that the call is still connected, as opposed to produce absolute silent, which can give the impression that, the call have been dropped
The silent frame will be produced only by an encoder with VAD enabled
The synthesized comfort noise only produced by CNI enabled vocoder

## Slide 7: Description 2
VAD and CNI can be enabled by either hardware config (DTX_ENABLE pin 5 TQFP) or as part of a control packet
The silence threshold value is -25 dBm in VAD algorithm
Each frame that exceeds this level will be classified as voice
If the frame level is less than -25 dBm, the voice or silence decision will be determined based upon various adaptive thresholds

## Slide 8: Echo Canceller

## Slide 9: Block Diagram
The vocoder employs an adaptive echo cancellation algorithm to cancel echoes of the decoder output present at the encoder input

## Slide 10: Description
The echo canceller is suitable for cancelling local echo caused by a 2-to-4 wire hybrid
The echo canceller can achieve echo cancellation of approximately 30 dB or more
The linear audio codecs will generally provide better performance than A-Law or U-Law codecs due to lower quantization noise

## Slide 11: DTMF Generation and Detection
Notes: Notes:
DTMF (Dual Tone Multiple Frequency)

## Slide 12: Block Diagram
The vocoder is capable of detecting, transmitting and synthesizing DTMF tones
Notes: Notes:
DTMF (Dual Tone Multiple Frequency)

## Slide 13: Description
When the encoder detects DTMF tones, the voice data field will contain the DTMF tone data
Additionaly, the encoder passes the DTMF data (within the regular voice data bits) so that normal DTMF tones pass seamlessly from encoder to decoder for synthesis
The decoder synthesizes a DTMF tone in response to reception of in-band DTMF tone frame or reception of a control packet with the DTMF word set

## Slide 14: Description 1
Each tone packet generates 20 ms of output tones
The length of output tones can be extended by repeating the tone packet
DTMF may be enabled or disabled through a control packet (enabled by default)

## Slide 15: Soft Decision Error Correction

## Slide 16: Block Diagram
Significant improvement in error correction performance can be added by setting up receiver so that the modulator is making a finer estimation prior to send it to decoder, this is called soft-decision decoding

## Slide 17: Description
The vocoder utilizes a 4-bit soft decision decoder, and the bits are defined as follows:
The user must implement circuitry at the receive end of the channel for making a finer (4 bit) estimation
Decision Value | Interpretation
0000 | Most confident 0
0111 | …
1000 | …
1111 | Most confident 1
Notes: Notes:
Algorithm for interpretation may be confidential for DVSI AMBE

## Slide 18: Description 1
The vocoder use different channel data (CHAND4) to specify channel data represented by 4 soft decision bits
The decoder will make the decision of whether or not a 1 or 0 is represented by the soft decision bits

## Slide 19: Noise Suppressor

## Slide 20: Description
The noise suppressor of the vocoder is used to reduce the effect of background noise in the encoder input signal
The noise suppressor is applied to both silence and voice frames, but not tone frames
When noise suppressor is started, it may take up to a few seconds to converge allowing for it to begin fully working
The noise suppressor is enabled by setting NS_ENABLE pin 7 TQFP

## Slide 21: Companding Using A-Law and U-Law

## Slide 22: Description
The vocoder support either 16-bit linear, 8-bit A-Law, or 8-bit U-Law formats
Given that A-Law and U-Law companding formats already incorporate some compression to reduce number of bits per sample, it is recommended to use 16-bit linear PCM data sampled at 8 kHz for maximum voice quality
The codec interfaces are provided for design engineer who is trying to fit pre-existing condition

## Slide 23: Description 1
To enable or disable companding and select the format, use either hardware pins as described in the following tables
CP_ENABLE | Pin 8 TQFP
Companding disabled | 0
Companding enabled | 1
CP_SELECT | Pin 9 TQFP
Select U-Law | 0
Select A-law | 1

## Slide 24: Summary

## Slide 25: Vocoder Special Functions
VAD and CNI
  VAD: detect period of silence on speaker end
  CNI: generate comfort noise on listener end to give a feeling that the call is still connected
Echo Canceller
  Adaptive echo cancellation to cancel echoes of the decoder output present at the encoder input
DTMF Detection and Generation
  The vocoder is capable of detecting, transmitting and synthesizing DTMF tones
  When the encoder detects DTMF tones, the DTMF tone data will be put in voice data field

## Slide 26: Vocoder Special Functions 1
Soft Decision Error Correction
  The vocoder utilizes a 4-bit soft decision decoder
  Need to implement circuitry at the receive end of the channel for making a finer (4 bit) estimation
  The decoder will make the decision of whether or not a 1 or 0 is represented by the soft decision bits
Noise Suppressor
  It is used to reduce the effect of background noise in the encoder input signal
Companding Using A-Law and U-Law
  The vocoder support either 16-bit linear, 8-bit A-Law, or 8-bit U-Law formats

## Slide 27: Discussion