## Slide 1: Secure Modem
Hardware Design – Audio Codec

## Slide 2: Contents
Audio Codec Block Diagram
Audio Codec Algorithm
Audio Codec Selection
Summary
Discussion

## Slide 3: Audio Codec Block Diagram

## Slide 4: Audio Codec Block Diagram
The vocoder can be configured to transmit and receive digitized speech to and from most linear, a-law, or u-law audio codec
The 16-bit linear audio codec are preferable over an a-law and u-law companding chips
Notes: Notes:
Companding (Compression and Expanding)
The 16-bit linear audio codec is preferable because the a-law and u-law chips are already incorporating some compression to reduce the number of bits per sample
Using a-law or u-law chips may reduce the overall voice quality, generated by the modem
Source:
AMBE-3000F_manual.pdf

## Slide 5: Audio Codec Algorithm
a-law
u-law
linear

## Slide 6: A-law
An ITU standard for converting analog data into digital form using Pulse Code Modulation.
It uses a companding technique that provides more quantizing steps at lower amplitude (volume) than a higher amplitude.
It is used in European 8-bit PCM digital communication systems
Notes: Source:
http://encyclopedia2.thefreedictionary.com/A-law+algorithm
http://en.wikipedia.org/wiki/A-law_algorithm

## Slide 7: A-law 1
A-law compression
Common A value=87.7
A-law expansion

## Slide 8: U-law
It is a form of logarithmic quantization or companding
It is based on the observation that many signals are statistically more likely to be near a low signal level than a high signal level
Therefore, it makes more sense to have more quantization points near a low level than a high level
In typical system, linear samples of 14 to 16 bits are companded to 8 bits
Used in North America and Japan
Notes: Source:
http://www.threejacks.com/?q=node/176

## Slide 9: U-law 1
U-law compression
Common μ value: 255
U-law expansion

## Slide 10: U-law 2
Exercise in MATLAB
  Compare avg error of U-law companding and linear companding

## Slide 11: Audio Codec Selection
Texas Instrument PCM3500
Texas Instrument TLV320AIC14

## Slide 12: PCM3500
Features
  16-bit ADC and DAC
  Sampling Freq
    7.2 to 26 kHz
  2.7 to 3.6V power supply
  Master or slave mode
TI PCM3500 Audio Codec
Slave Mode
Master Mode

## Slide 13: PCM3500 1
Interfacing with AMBE3000
  Operated as Master
  Using McBSP interface
  Using 3.3V power supply
AMBE3000 and Audio Codec

## Slide 14: TLV320AIC14
Features
  16-bit ADC and DAC
  Sampling Freq
    26kHz with IIR/FIR filter
    104kHz without filter
  1.7 to 3.6V power supply
TI TLV320AIC14 Audio Codec

## Slide 15: TLV320AIC14
Interfacing with AMBE3000
  Using SPI interface
  Using 3.3V power supply
  Audio codec can be programmed via packet from AMBE3000
AMBE3000 and Audio Codec

## Slide 16: Summary

## Slide 17: Audio Codec
In order to process audio signal, vocoder need audio codec to digitized, analog audio
Audio codec performs companding (compression and expanding) to reduce size of digitized audio signal
Common companding algorithm:
  Linear codec
  A-law codec
  U-law codec

## Slide 18: Audio Codec 1
A-law and U-law codec have better performance than linear codec because have more quantization points near low level (where many signals are located)
However, for the vocoder, it is preferable to use 16-bit linear codec than either A-law or U-law codec, because they are lossy codec
They are two option of audio codec for AMBE3000:
  PCM3500
  TLV320AIC14 (suggested by reference design)

## Slide 19: Discussion