## Slide 1: Secure Modem
Hardware Design – The Vocoder

## Slide 2: Contents
Vocoder Overview
Vocoder in Radio Modem
AMBE Vocoder
Summary
Discussion

## Slide 3: Vocoder Overview
What is Vocoder
History of Vocoder
How Vocoder Works
Vocoder Application

## Slide 4: Vocoder Description
The vocoder is an electronic device that analyzes the human voice, breaking it up into its component parts
The voder is a similar device that synthesizes a human voice
More often than not, vocoder and voder are combined in one unit
Early 1970s electronic music vocoder
Vocoder chips
Notes: Source:
http://www.ieeeghn.org/wiki/index.php/Vocoders_and_Voders

## Slide 5: History of Vocoder
Motivation:
  Bandwidth restrictions for transmission of a complete human speech
  Potential for undesirable eavesdropping in traditional analog devices
In response to those issues:
  Homer W. Dudley devised a system for vocal communication while working at Bell Labs
  Described in detail in his 1935 patent application was the device known as the vocoder
Notes: Notes:
Human freq. 80 Hz to 14 kHz but telephone call freq. only 340 Hz to 3.4 kHz
Source:
http://community.wvu.edu/~ndw010/projects/vocoder/
http://en.wikipedia.org/wiki/Wideband_audio

## Slide 6: How Vocoder Works
Encoder
  Speech waveform is passed through a parallel bank of BPF
  After BPF, the filtered signal is passed to envelope follower to approximate the average amplitude of that band
  BPF and envelope follower produce a rough frequency spectrum of speech waveform
  Fundamental detector detects instantaneous fundamental frequency of speech signal
  All those signals are combined to produce an encoded speech waveform
Simplified block diagram of voice encoder
Notes: Source:
http://community.wvu.edu/~ndw010/projects/vocoder/

## Slide 7: How Vocoder Works 1
Norm. freq. spectrum of a female speech signal
fs = 44.1kHz
Comparison of FFT spectra and filter output

## Slide 8: How Vocoder Works 2
Decoder
  The incoming signal is demultiplexed and each signal is routed to the appropriate block
  Signal representing fundamental freq. is routed to VCO, which generates a waveform at fundamental freq.
  This waveform then mixed with white noise signal and passed to BPFs
Simplified block diagram of voice decoder
Notes: Notes:
VCO (Voltage Controlled Oscillator)
Source:
http://community.wvu.edu/~ndw010/projects/vocoder/

## Slide 9: How Vocoder Works 3
Decoder cont.
  The incoming signal representing the band levels, each drive the gain of one of VCA at the output of each filter
  Each of the outputs are then mixed together to produce resynthesized speech signal
Notes: Notes:
VCA (Voltage Controlled Amplifier)

## Slide 10: Vocoder Application
Digital voice scrambling and encryption
VoIP system
Artistic musical effect
Cochlear implants
Etc.

## Slide 11: Vocoder in Radio Modem
Commercial Radio Modem
Vocoder

## Slide 12: Commercial Radio Modem
AOR ARD9900
  Digital data and voice over analog radio
  Interfacing TX/RX (MIC and SP)
  Using AMBE2020 vocoder
Radio Modem AOR ARD9900

## Slide 13: The Vocoder
Vocoder on AOR ARD9900
8KHz Sampling Voice
2400bps
+
1200bps FEC
Vocoder on AOR ARD9900

## Slide 14: AMBE Vocoder
AMBE2020 chip
AMBE3000 chip

## Slide 15: Comparison of AMBE Chips
AMBE2020 Layout
AMBE3000 Layout

## Slide 16: Comparison of AMBE Chips 1
AMBE2020 specs:
  Operation: Half-duplex
  Data rates: 2.0 to 9.6 kbps
  FEC rates: 50 to 7200 bps
  AMBE+ compression
  Interfaces:
    Serial port for channel interface
    Serial port for codec interface
AMBE3000 specs:
  Operation: Half or Full-duplex
  Data rates: 2.0 to 9.6 kbps
  FEC rates: 50 to 7200 bps
  AMBE+2 compression
  Interfaces:
    SPI (speech data samples interface only)
    McBSP serial port
    UART
    Parallel port
Notes: AMBE2020
Channel interface is general term for interface for compressed bits coming from encoder and going to decoder

## Slide 17: Comparison of AMBE Chips 2
AMBE2020 HDK Block Diagram
AMBE3000 HDK Block Diagram

## Slide 18: Comparison of AMBE Chips 3
AMBE2020 HDK:
  Vocoder
  Audio Codec
  Controller
  Vocoder and Controller interface IC
AMBE3000 HDK:
  Vocoder
  Audio Codec
  Controller

## Slide 19: Summary

## Slide 20: The Vocoder
Vocoder is a device that analyzes and synthesizes human voice
Main motivation of vocoder creation is bandwidth restriction for transmission of a complete human speech
Encoder and decoder process

## Slide 21: The Vocoder 1
Comparison of AMBE chips (AMBE2020 and AMBE3000)
AMBE2020 | AMBE3000
Half-duplex | Half or full-duplex
Data rates: 2.0 – 9.6 kbps | Data rates: 2.0 – 9.6 kbps
FEC rates: 50 – 7200 kbps | FEC rates: 50 – 7200 kbps
AMBE+ compression | AMBE2+ compression
Interfaces: serial | Interfaces: serial and parallel
HDK: vocoder, audio codec, controller, and FPGA (vocoder and controller interface) | HDK: vocoder, audio codec, and controller

## Slide 22: Discussion